## Slide 1
BY ELODIE HIGGINS h
ACCELERATOR PHYSICS GROUP,
THE UNIVERSITY OF MELBOURNE
.
UNDER THE SUPERVISION OF SUZIE SHEEHY
OPTIMISING GANTRY DESIGNS FOR HADRON THERAPY

## Slide 2
OVERVIEW
Advantages and limitations of hadron therapy
Gantry designs
Project description
Overview of accelerator physics & beam line optics
Results
Summary
MedAustron, Austria
Pronton/carbon ion synchrotron

## Slide 3
1
CANCER TREATMENTS
17 million/yr diagnosed with cancer
~50% will receive radiotherapy treatment
External ‘beam’ Radiotherapy
  High energy photons
  Electrons
  Hadrons
  Deposit dose over tumour
  Minimise damage to healthy cells
  Accessible to suitable patients

## Slide 4
2
ADVANTAGES OF HADRON THERAPY
Bragg peak → Precise depth and position control
Good dose conformity and increased RBE
  Peak depth increases with energy
  Carbon ions have higher RBE than proton ions
  Reduces:
    Overall toxicity
    Long term side effects
  Smaller energy required for same depth of Proton ions

## Slide 5
3
OPPORTUNITIES & LIMITATIONS
Heidelberg Carbon ion gantry
Could improve therapeutic outcomes of 15-20% patients receiving radiotherapy
  Only reaching 20,000/yr (80% proton ions)
Delivery must be very precise to minimise toxicity
Rotating gantry around patient:
  Very expensive
  Massive facilities
  Long and difficult to run

## Slide 6
4
GANTRY DESIGNS
Normal magnets: Heidelberg gantry: 25m in length, 13m in diameter and an overall mass of 600 tonnes.
Superconducting (SC) magnets: NIRS gantry: 13m in length, 11m in diameter and an overall mass of 200 tonnes.
Fixed Field Alternating gradient (FFA) optics with normal or SC magnets:
  Multiple energies
  Smaller size: FFA SC gantry proposed by Dr Trbojevic: diameter ~8 m, mass ~30 tonnes.
Rigidity: 𝑅=𝐵𝜌=

## Slide 7
5
PROJECT OUTLINE
Design an FFA bend to accept the energy range of 0.5 – 4 MeV proton accelerator, the Pelletron beam, without changing magnet strength
This test beamline will be the first built of its kind
Considerations:
  Optimise the beam envelope for entire energy range:
    Optimise the cell configuration
    Have reasonable magnet strengths
    Lattice size must fit in the space available (< 2m)
    Ensure a reasonable magnet aperture (5-10cm)

## Slide 8
6
CELL COMPONENTS
A lattice is a sequence of repeating cells.
Quadrupoles:
QF focuses, QD defocuses
Dipoles:
Bend the beam,
Drifts: empty space

## Slide 9
7
DEFINING ACCELERATOR PHYSICS TERMINOLOGY
Orbit function
Betatron Function (, )
Dispersion ( or )
Solution to Hill’s equation:
Hill’s equation:
ALL THREE COMPONENTS CONTRIBUTE TO MAGNET APERTURE SIZE

## Slide 10
8
NORMAL vs. FFA BEAMLINE COMPONENTS
Normal beam line: Same for all energies until particle is lost
FFA beam line: Different energy particles adopt a different physical path. Particles focused/defocused for the reference energy magnet strength

## Slide 11
9
FFA OPTICS
  Large energy acceptance:
    Various energies allowed through beamline components
    WITHOUT ramping magnets
  Permanent magnets can be used:
    Cheaper and smaller
    Easier to run

## Slide 12
10
METHOD
2. Constructed stable focusing bends
BMAD: “object oriented, open source, subroutine library for relativistic charged particle dynamics simulations in accelerators”
Constructed stable quadrupole lattices:
FODO
Doublet
Triplet

## Slide 13
1
COMBINED MAGNETS (45◦, )
3. Constructed stable focusing bends with combined magnets
  Less magnets in the lattice (reduces cost and weight)
  Quadrupole magnet placed off axis
    Magnetic field gradient created adds a dipole field
FODO
Doublet
Triplet
1

## Slide 14
1
2
H
SELECTING CELL CONFIGURATION
The smallest normalised dispersion minimises the dispersion and betatron function of the lattice

## Slide 15
1
3
  Doublet configuration selected:
    Space for beam line components
  Parameters that were configured
    Focusing/Defocusing (k) strengths
    Position of reference energy
    Length of components and drift spaces
      Defines the dipole strength for specific bend
DOUBLET CONFIGURATION

## Slide 16
1
4
PARAMETERISATION
Ref E is the energy the magnets will be scaled to:
  Higher ref E → smaller orbit excursion → smaller relevant energy range
Orbit excursion of 40.91 mm and full Pelletron energy range (0.5-4MeV) selected:
Ref E = 1.5 MeV, k =
Focusing/defocusing strength:
  Higher k → smaller orbit excursion → smaller relevant energy range

## Slide 17
1
5
ORBIT OFFSET RESULTS
REFERENCE ENERGY = 1.5 MeV, k=
= fractional energy change of particles from the reference energy
Relates to: 4 MeV
Orbit offset max: +33.0 mm from Ref E
= -42.5 % Relates to: 0.5 MeV
Orbit offset max:
-7.9 mm from Ref E

## Slide 18
1
6
Orbit excursion = 40.9 mm (offset max = 33.0 mm; min = -7.9 mm)
Amplitude of oscillation = m
𝜖=8 𝜋 mm mrad*
Betatron oscillation = 5.013 mm
Magnet aperture required = 50.94 mm
KEY RESULTS

## Slide 19
1
NEXT CHALLENGES
Implementation into the Pelletron:
  Optimise a matching section
Scaling the system to therapeutic energies:
  Simulate a bend accepting:
    50-200 MeV proton ions
    1101-4632 MeV carbon ions
7

## Slide 20
1
8
SUMMARY
1.5 million patients could benefit from hadron therapy
Considered novel FFA technology
FFA bend successfully simulated
  0.5-4MeV energy in 5.1cm aperture
Test beamline to be built at the University:
  First time such technology will be built!
  Matching section required

## Slide 21
ACKNOWLEDGEMENTS

## Slide 22
THANK YOU, h
ANY QUESTIONS?
.

## Slide 23
SPREAD OUT BRAGG PEAK
As energy increases, so does the depth of the peak
Extremely precise, therefore a ‘Spread Out Bragg Peak’ (SOBP) is needed to span width of the tumour