## Slide 1: Status of FFA accelerator in Kyushu University
Faculty of Engineering, Kyushu University
Yujiro Yonemura

## Slide 2: Contents
Overview of accelerator facility of Kyushu University
Status of beam commissioning
Experimental results of beam extraction
Summary

## Slide 3: Overview of Accelerator Facility
Internal
Ion Source
Cyclotron
10 MeV Proton
Experimental
Hall
125 MeV Proton
8 MV Tandem Accelerator
Ion Source
(p, d, Heavy Ion)
12 MeV Proton
or Heavy Ion
150MeV Proton or Heavy Ion beam
150 MeV
FFA

## Slide 4: Construction status of accelerator facility
150 MeV FFA
Experimental hall
1st Stage
Almost completed
Beam commissioning of the 150 MeV FFA accelerator and the tandem accelerator have been completed. In order to increase beam energy and current, optimization of operating parameters and improvements of equipment have been carried out.
2nd Stage
Applying for a budget
Several projects are planned in the future.
The improvement of the magnets of the main ring
the expansion of experimental hall
  Construction of proton and neutron Irradiation room
  Neutron source with the modified ERIT ring
the demonstration of heavy ion injection and acceleration with FFA accelerator
Tandem accelerator
Details will be reported later in my presentation.

## Slide 5: Status of Beam Commissioning(1)
2016-2018
Construction and operation test of the beam extraction system
operation test of the extraction kicker and the extraction septum has been successfully performed. All technical troubles of power sources and water-cooling system were resolved by repairing or replacing failed devices.
(reported in FFA workshop 2018)
2019
Jan. – May
Beam acceleration test / Tune measurement
Jun.
Installing additional magnetic pole
(tune correction patch)
Beam acceleration
Jul.
Aug.
Driver amplifier broke down, and it was temporarily replaced with an amplifier with low output power.
Sep.
Beam acceleration up to final energy
Position adjustment of extraction kicker
Optimization of timing system
Operation time
in 2019
~ about 27 days

## Slide 6: Status of Beam Commissioning(2)
2019 Oct. –
2020 Feb.
Installation of additional beam monitor
Hight power test of extraction septum and kicker
Beam extraction
Operation was suspended due to Covid-19
Apr. – Aug.
Sep. – Nov.
Maintenance period
Repair of water-cooling system
Mar.
Water-cooling system of injector cyclotron broke down
Commissioning schedule
Jan.-Mar.
2021
Dec.
Beam commissioning
Beam experiment for extraction

## Slide 7: Experimental condition of beam extraction
Particle: Proton from injector cyclotron
Injection energy: 10 MeV
Extraction energy: 75 MeV ( 1st Stage), 100 MeV (2nd Stage)
Repetition rate: 20 Hz

## Slide 8: Configuration of Beam Extraction System
Phase [deg.]
x [m]
Extraction
Kicker
Extraction
Septum
Extraction method : Fast extraction
Phase advance between kicker and septum: 440 deg.(4 cells) ≅ 3 p

## Slide 9: Timing chart of beam acceleration and Extraction
Gap Voltage | 3 .0 kV/cavity
RF frequency | 1.5 – 4.2 MHz
Synchronous Phase | 20 deg.
Repetition rate:
20 Hz
Acceleration cycle:
50 Hz (20 ms)
75 MeV

## Slide 10: Timing system
Agilent 33210A
Function/Arbitrary Generator
Agilent 33522A
Function/Arbitrary Generator
Agilent 33522A
Function/Arbitrary Generator
Agilent 33522A
Function/Arbitrary Generator
Agilent 33522A
Function/Arbitrary Generator
Cyclotron RF
Pulse Ion Source
Beam Chopper
Main ring RF
Injection Bump #1
Injection Bump #2
Extraction Kicker
Extraction Septum
Tektronix
AWG 2021
The timing was adjusted so that the beam current was maximized.

## Slide 11: Layout of beam monitors
Copper electrode
900 mm
Destructive beam monitor
Extraction magnetic septum

## Slide 12: Beam profile monitor at extraction septum
Extraction
Septum
Movable beam shutter #1 (Inlet)
Movable beam shutter #2 (Outlet)
circulating beam
extracted beam

## Slide 13: Vertical tune monitor
Aluminum electrode
Electric Insulation rod
Installed vertical tune monitor in vacuum chamber
It is employed as a bunch monitor

## Slide 14: Position adjustment system of extraction kicker
Extraction kicker installed in vacuum chamber
Extraction kicker magnet
Position adjustment system
(turntable and
rod for moving turntable)
Radial direction
turntable
turntable
rod
rod
rod
rod
To adjust position and angle of the extraction kicker magnets, the turntable that moves in the radial direction was installed.

## Slide 15: Optimization of position and excitation timing of extraction kicker magnet
The beam profile at the inlet of the extraction septum was measured
by changing the position and excitation timing of the extraction kicker magnet.
Optimum conditions for the position and the timing are experimentally determined.
Measured beam profile with respect to the position of kicker magnet
Measured beam profile with respect to the excitation timing of kicker magnet

## Slide 16: Optimization of position and dimensions of additional magnetic pole
Dimension
300 x 140 x 15
In order to reduce beam loss during acceleration, iron plates that reduce variation of vertical tune are installed in both side of the magnet.
Position adjustable plate to control vertical tune near the extraction septum.
Additional magnetic pole to control vertical tune during acceleration.

## Slide 17: Experimental results
Optimum position are experimentally determined.
Beam loss has significantly been reduced.
Small beam loss still exists.
Additional optimization is needed.
Beam loss
The output signal of the bunch monitor was measured
by changing the dimensions and position of the additional magnetic plate.
Beam loss
Additional magnetic pole
Position adjustable plate
Details will be reported
in Mr. Waga’s presentation.
The beam loss was minimized if the additional magnetic pole consists of 4 iron plates.

## Slide 18: Beam extraction
In order to increase the efficiency of beam extraction,
the optimization of position and angle of extraction magnetic septum are required.
The optimization will be started in the next beam experiment.
163 pA
87 pA
Inlet of Extraction septum: 36 pA
Extracted beam: 5 ~ 10 pA
Beam loss was cased by error field of
The extraction septum magnet
Beam extraction has been successfully performed.
Flat top
(75 MeV)
The extraction septum magnet and extraction kicker are excited.
The extracted beam current is measured with current monitor at the extraction port.

## Slide 19: Future plan
Improvement of the magnets of the main ring
  Additional return yoke
  Magnetic shield
Expansion of experimental hall
  Construction of proton and neutron Irradiation room
  Neutron source with the modified ERIT ring
Demonstration of heavy Ion acceleration with FFA
In Kyushu University, several projects are planned in the future.
Applying for a budget

## Slide 20: Improvement of the magnet
Additional return yoke and Magnetic shield
Optimization of shape of additional magnetic pole
Details will be reported in Mr. Waga’s presentation
In order to reduce the tune variation,
the study on the improvement of magnet of 150 MeV FFA has been conducted.

## Slide 21: Neutron source with 100 MeV ERIT ring
Proton beam from FFA
To promote study of nuclear physics, neutron science and medical field,
we are planning to relocate the ERIT ring from Kyoto University to Kyushu University
and remodel it to the 100 MeV ERIT ring.
A budget for relocation has been applied for.
100 MeV ERIT ring

## Slide 22: Demonstration of heavy Ion acceleration with FFA accelerator
Injector: 8 MV tandem accelerator
Charge exchange injection （He1+  He2+）
Injection Energy of He1+ : 14 MeV
Performance test of Heavy Ion source has been almost completed.
Mechanical design of charge converting film will be started.
He1+
He2+
In order to measure double differential cross section of compound nucleus in low energy region,
we are planning to accelerate heavy ion beam with the 150 MeV FFA accelerator.
Charge converting Film

## Slide 23: Construction of proton and neutron Irradiation room
The irradiation room will be used in the field of life science, material science, agriculture and neutron science.
A budget for construction has been applied for.

## Slide 24: Summary
Beam extraction has been successfully performed.
Beam loss has significantly been reduced with the additional magnetic poles.
In order to increase the efficiency of beam extraction,
optimization of position and angle of extraction septum is required.